## Slide 1: LSTN: A Linear Model of Industrial Production Process for Demand Response
Ruike Lyu, Hongye Guo, Qixin Chen et al.
Department of Electrical Engineering,
Tsinghua University, Beijing, China
Paper №: A8709RL
1/9

## Slide 2: Introduction
Chart: 
104520 MW
5940 MW
Electricity load (10MW)
Output of wind/PV power (10MW)
Low output during peak load
Electricity load and wind/PV power output curve on Aug 3, 2020, Jiangsu Province, China
Demand response (DR) has huge potential for maintaining demand-supply balance
Why industrial users?
Large response volume (MWs)
Sensitive to the prices
Ability to implement DR
Why demand response?
Cost-effective for securing electricity supply in the power system
2 /9

## Slide 3: Introduction
Why industrial users?
Industrial Production Processes (IPPs).
Contributes most energy consumption of typical industrial users
Exists technical constraints and production targets
Modelled by: state-task network (STN), resource-task network…
MILP formulations for the on/off operating states of devices
STN modelling
3 /9

## Slide 4: Objectives
Linear model instead of MILP-based models
Overcome computation complexity issues
Increase production model accuracy
Easier to embed into existing models
Linear constraints are more “friendly” for power system dispatch models
Power is discrete, but the energy integrated over a time interval can be close to continuous
An analogy:
PWM rectification
(Pulse Width
Modulation)
4 /9

## Slide 5: Methodology
Use operating time as the variable
Under the time intervals of DR (e.g. hour by hour)
Change the variable: device operating state -> operating time
Feasible; up to the industrial user to implement
The industrial user implements the operation of the devices
hour | 1 | 2 | 3 | …
state of device 1 | on | on | off | …
hour | 1 | 2 | 3 | …
on-time of device 1 | 1h | 0.8h | 0h | …
off-time of device 1 | 0h | 0.2h | 1h | 
STN
LSTN: linear STN
5 /9

## Slide 6: Methodology
Use operating time as the variable
A linear model
Fast to compute
Suits aggregation
Accuracy?
6 /9
A two-layer framework for aggregating
industrial facilities for large-scale DR
No need to worry about the equations :)

## Slide 7: Case Study
Tested using electricity price of PJM and parameters of a steel powder manufacturing.
“True” value: STN-2min (it takes 2 min to switch)
7 /9

## Slide 8: Results
Modeling Accuracy
Computational Time
LSTN: red True: black
STN-60min: Computationally intractable with more than 80 industrial facilities
8/9
LSTN: Computationally tractable with 2000 industrial facilities or more

## Slide 9: Conclusions
LSTN: Linear STN instead of MILP-based models
Overcome computation complexity issues
Increased model accuracy
Easier to embed into dispatch models
Power is discrete, but the energy integrated over a time interval can be close to continuous!
An analogy: PWM rectification
9/9
My email: lrk21@mails.tsinghua.edu.cn